## Slide 1
L2 - Knowledge sharing
FT 517, 523, 792, 1796
TDD/FDD
Artur Ekert
22.04.2020

## Slide 2
Abbreviations
ACK Acknowledgment
ATB AdaptiveTransmissionBandwidth
BLER Block Error Rate
CRC cyclicredundancycheck
CSI-RS Channel StateInformation-Reference Signals
CQI Channel QualityIndicator
HARQ HybridAutomatic RetransmissionRequest
ILLA Inner LoopLink Adaptation
MCS Modulationand CodingScheme
SU-MIMO Single User Multiple-Input Multiple-Output
MU-MIMO Multi User Multiple-Input Multiple-Output
NACK NegativeAcknowledgment
OLLA Open LoopLink Adapatation
PHR Power Headroom Report
PTRS PTRS Phase Tracking Reference Signa
QAM QuadratureAmplitudeModulation
QPSK QuadraturePhaseShiftKeying
SINR Signalto Interferenceplus NoiseRatio

## Slide 3
Presentation Plan
Where is what you’re looking for
BIP L1L2
Wireshark
TTI trace
TTI trace decoding
Sherpa
DDR4 Capture
MUE TDD logs analysis
MUE FDD logs analysis
eLA FDD logs analysis
Q&A
Useful links

## Slide 4
Basic Knowledge
5GC000523 TDD scheduler for Multi-UE support
5GC000517 Uplink and downlink link adaptation
5GC001796 Enhanced Link Adaptation procedures
5GC000792 FDD scheduler for Multi-UE support

## Slide 5
Where is what you’re looking for?

## Slide 6
Where is what you’re looking for?
 | Snapshot/ Journalctl | BTSLog | UE Log | X2 | S1/Ng | BIP/Egen | L2-PS TTI | SHERPA | DDR | RFSW calibration
Tput | X | X | X | X | X | X | X | X |  | 
Attach | X | X | X | X | X | X | X | X |  | 
Detatch | X | X | X | X | X | X | X | X |  | 
Reset | X | X |  |  |  |  |  |  |  | 
PMStats | X |  |  |  |  |  |  |  |  | 
RACH | X |  | X |  |  | X | X | X | X | X
Beam Mgmt | X |  |  |  |  | X | X | X |  | X
GPS | X | X |  |  |  |  |  |  |  | 
NotOnAir | X | X |  | X | X |  |  |  |  | 
https://confluence.int.net.nokia.com/display/CV/5gNB+Logs+collection+and+troubleshooting

## Slide 7
How to Collet BIP L1-L2 log – Red Rock Canyon

## Slide 8
How to Collet BIP L1-L2 log – Red Rock Canyon
On ASIK
#dbgrrc mirror sport <port_num> dport <port_num> <e|d> [i|e|b]
[vlan <vlan_number>]
with:
e|d standing for enable|disable
i|e|b standing for ingress|egress|both
<port_num> : RRC port
Eexample : to check what is sent from eth2 BB2 which should
be received by RRC EIF2 port (source port 15)
to ABIL master xeon (dest port 20) we performed,
on ASIK following commands
#dbgrrc mirror sport 15 dport 20 e b
#tcpdump port 20
https://confluence.int.net.nokia.com/display/OPSW1/ASIK+Red+Rock+Canyon+%28RRC%29+ports+distribution
https://confluence.int.net.nokia.com/display/MANO/ASIK

## Slide 9
How to Collet BIP L1-L2 log – data paths

## Slide 10
ASIK bsh/bget command (substitute of ssh / scp)
bsh [-t <timeout_in_sec>] [-b] [[<domainId>:]<boardId>:]<socId> [<command> [args...]]
bsh 0 sesja na XEON master ASIKa (192.168.253.16)
bsh 1 sesja na XEON slave ASIKa (192.168.253.17)
bsh 1:0 sesja na XEON A ABILa (192.168.253.20)
bsh 1:1 sesja na XEON B ABILa (192.168.253.21)
bsh 1:2 sesja na Lonera ABILa (192.168.253.22)
bget [-t <timeout_in_sec>] [[<domainId>:]<boardId>:]<socId> <remote-file> <local-dir>
eg. To download log.txt from Loner to ASIK Master tmp dir, you can use command:
root@fct-0a:~ >bget 1:2 /tmp/log.txt /tmp/

## Slide 11
How to Collet BIP L1-L2 log
Download mirror scripts: \\eseefsn50.emea.nsn-net.net\rotta4internal\5G\Oulu_L3_CAMP\gnbMirroring
Copy scripts to ASIK Xeon Master: /ffs/run/config/scripts/
Configure parameters, and start logs collecting – edit gnbMirroringConfig.sh
  Capturing on ASIK
    Add execution right to the file: chmod +x gnbMirroring.sh
    Run script: ./gnbMirroring.sh -> capturing will be stopped after „CAPTURING_TIME_SECONDS”

## Slide 12
How to Collet BIP L1-L2 log
Capturing on external sniffer
    Add execution right to the file: $chmod +x gnbMirroring.sh
    Run script: $./gnbMirroring.sh ->
      You can execute command remotly eg. sshpass -p oZPS0POrRieRtu ssh -A -t toor4nsn@10.42.555.444 '/ffs/run/config/scripts/gnbMirroring.sh’
    Start tcpdump on connected to ASIC interface eg. #tcpdump -i ens1f1 -w name_of_file.pcap -C 100M
    Stop collecting after the test (kill tcpdump process)
Configure MTU on network interface to 9216
# ifconfig ens1f1 mtu 9216
Or edit interface config file

## Slide 13
How build tcpdump/WS capture filter
Capture BIP without any filter
Open it and decode
Check payload of msg which is needed/not needed
Build tcpdump capture command:
tcpdump -i ens1f0 'ether[0x18:2]!=0x122 ' -w log.pcap
Example pcap filter for FDD SA:
tcpdump -i ens1f0 'ether[0x18:2]!=0x122 && ether[0x18:2]!=0x240 && ether[0x18:2]!=0x127' -w log.pcap
Moore complex bash script to read/write filtered .pcap file:
Count of crc err in harqU msg:
tcpdump -r BIP.pcap 'ether[0x18:2] = 0x0218 && ether[0x38:1] = 0x01' -w tmp.pcap; capinfos tmp.pcap -c –M; rm -f tmp.pcap

## Slide 14
How to decode L1-L2 BIP .pcap
Tools:
Wireshark LTE-5G
Luashark -> Can be download from WFT or Artifactory
How to run Luashark? -> execute command in cmd: C:\Program Files\Wireshark\Wireshark.exe" -X lua_script:C:\path\to\luashark.lua C:\path\to\file.pcap
You can use WiresharkStarter, or config WS Shortcut:
In „Target” field, paste execute command

## Slide 15
How to decode L1-L2 BIP .pcap – 5G-Wireshark
5G-Wireshark (nokia-sbell) -> NOT SUPPORTED
Download bip_dll_v2.1.zip which can be download from the same location
Replace old bip.dll with a proper to your gNB SW release
(do not forget to change ext of new file!):
Start 5G-Wireshark and decode your .pcap in a few seconds 

## Slide 16
How to decode L1-L2 BIP .pcap – 5G-Wireshark
Configure WS preferences:
Always use the only proper layout!
Change protocol settings:

## Slide 17
How to decode L1-L2 BIP .pcap – 5G-Wireshark
3. Change protocol settings:

## Slide 18
How to decode L1-L2 BIP .pcap – 5G-Wireshark
4. Display filter save (Add display filter button)

## Slide 19
How to decode L1-L2 BIP .pcap – 5G-Wireshark
5. Coloring Rules
You can use build before display filter
to mark packages

## Slide 20
How to decode L1-L2 BIP .pcap – 5G-Wireshark
6. Configuration Profiles
All personal configs will be saved under new profile

## Slide 21
How to capture L2-PS TTI traces - ABIL
root@fct-4a:~ >bsh 1:0
root@asp-5a:~ >cd /opt/tools/ttiTrace
root@asp-5a:~ >./eventsCollect.sh
Traces will be saved in /var/eventsTrace/
Unpack files: tar xvzf /var/eventsTrace/L2TtiTrace_EventsSnapshot.bin.1.tar.gz
Decode ./eventDecoder L2TtiTrace_EventsSnapshot.bin.1 ./
You should received 3 .csv files
To speedup capturing you can use attached script 
Copy it to ABIL Master (bsh 1:0) and execute ./gnb_tti_traces_v3.sh start/stop
It will capture and decode all files
https://confluence.int.net.nokia.com/display/5GFTUlm/TTI+traces#TTItraces-RemarktoeventSnapshotDecoder

## Slide 22
How to capture L2-PS TTI traces - Sniffer
To capture TTI traces at sniffer, we need to use L2-PS Events Streaming mode
To activate tti traces streaming mode, we have 2 ways:
  O&M
    In Web EM -> Diagnostic -> Debug Tracing
    Configure IPs
    Configure Uplane traces
LABNET
10.42.61.148
10.44.181.210

## Slide 23
How to capture L2-PS TTI traces - Sniffer
  b. ASIK commands
    Enable icom mode: # /opt/trs/bin/trs-vppctl icom 630_mode enable
    Set Classical mode: # /opt/trs/bin/trs-vppctl icom classical_mode enable
    Configure stream Ips: # /opt/trs/bin/trs-vppctl icom set_stream_conf src_ip 10.44.181.210 dst_ip 10.42.61.148 dscp 32 dst_port 5678
    Note: IPs used in command should be pingable in both directions.
    Check L2-PS node ID (9274, 9018, 8761, 5178, 4922, 4666)
    START traces:
    # curl -i -H "Content-Type: application/json" -X POST -d '{"key":{"nodeId":9274, "upSw":"l2ps", "traceType":"component"},"data":{ "state":"start", "eqId":537395200, "pciList":"[50]" }}' http://127.0.0.1:8008/troubleshooting/l2Stream
    If needed STOP tti trace streaming:
    # curl -i -H "Content-Type: application/json" -X POST -d '{"key":{"nodeId":9274, "upSw":"l2ps", "traceType":"component"},"data":{ "state":"stop", "eqId":537395200, "pciList":"[50]" }}' http://127.0.0.1:8008/troubleshooting/l2Stream
    Start tcpdump at sniffer on configured interface: #tcpdump -i ens255f0 -u port 5678 -w tti.pcap

## Slide 24
How to capture L2-PS TTI traces - Sniffer
b. v2. To faster setup, you can use gNBMACTTI tool, developed by KRD (for Classical only!).
You can use Your PR as a sniffer, if gNB is pingable from PC 
Replace „PC IP” with ip of your network adapter
Press „START MACTTI”
Chose Interface ID – in my case it is =4
To stop press „Stop MACTTI”

## Slide 25
How to decode TTI traces (.pcap)
You need machine with installed Centos 8, or Debian 9
Download tool ttitrace-X.YYY.ZZZ.txz from WFT, or directly from artifactory
Extract it
Add execution right: # chmod +x ./decodeAndAnnalyze
Go to ./decodeAndAnalyze/bin/
To decode .pcap file execute command: #./eventDecoder /path/to/ttitraces.pcap filename
You will get 3 .csv files: .dl.csv, .ul.csv, .dlAndUl.csv
Files are in format: Event_name:headers,values
To have more use full format to analysis, we need to convert it again. To do it we can use Bipper

## Slide 26
How to decode TTI traces - Bipper
You can download it from here
Go to TTI TRACE tab, choose .csv file to decode and start decoding:
Output file can be opened in excel
Data -> From Tex/CSV -> choose „comma” as Delimiter, and Load

## Slide 27
How to decode TTI traces - Bipper

## Slide 28
How to capture L2 Sherpa traces - Sniffer
To capture Sherpa traces at sniffer, we need to use L2-PS Sherpa Streaming mode
To activate tti traces streaming mode, we have 2 ways:
  O&M
    In WeB EM -> Diagnostic -> Debug Tracing
    Configure IPs
    Configure Uplane Sherpa
LABNET
10.42.61.148
10.44.181.210

## Slide 29
How to capture L2 Sherpa traces - Sniffer
  2. You can use similar ASIK commands, as in TTI logs collecting case
    Enable icom mode: # /opt/trs/bin/trs-vppctl icom 630_mode enable
    Set Classical mode: # /opt/trs/bin/trs-vppctl icom classical_mode enable
    Configure stream Ips: # /opt/trs/bin/trs-vppctl icom set_stream_conf src_ip 10.44.181.210 dst_ip 10.42.61.148 dscp 32 dst_port 5678
    Note: IPs used in command should be pingable in both directions.
    Check L2-PS node ID (9274, 9018, 8761, 5178, 4922, 4666)
    START traces:
    # curl -i -H "Content-Type: application/json" -X POST -d '{"key":{"nodeId":9274, "upSw":"l2ps", "traceType":"sherpa"},"data":{ "state":"start", "eqId":537395200, "pciList":"[50]" }}' http://127.0.0.1:8008/troubleshooting/l2Stream
    If needed STOP tti trace streaming:
    # curl -i -H "Content-Type: application/json" -X POST -d '{"key":{"nodeId":9274, "upSw":"l2ps", "traceType":"sherpa"},"data":{ "state":"stop", "eqId":537395200, "pciList":"[50]" }}' http://127.0.0.1:8008/troubleshooting/l2Stream
    Start tcpdump at sniffer on configured interface: #tcpdump -i ens255f0 -u port 5678 -w sherpa.pcap

## Slide 30
How to capture L2 Sherpa traces - Sniffer
b. v2. To faster setup, you can use gNBMACTTI tool, developed by KRD.
You can use Your PR as a sniffer, if gNB is pingable from PC 
Replace „PC IP” with ip of your network adapter
Press „START MACTTI”
Chose Interface ID – in my case it is =4
To stop press „Stop MACTTI”

## Slide 31
How to capture Sherpa traces
How to get license, logs analysis:
https://confluence.int.net.nokia.com/pages/viewpage.action?spaceKey=5GSH&title=Trace+Analysis+005%3A+How+to+use+Sherpa
Config Sherpa traces from O&M:
https://confluence.int.net.nokia.com/pages/viewpage.action?spaceKey=CSRNS5G&title=How+to+get+traces+with+Sherpa
Sherpa training video:
https://nokiaedu.webex.com/nokiaedu/lsr.php?RCID=30372ca62a1748eebcd4e94d06a79813
+ one more confluence:
https://confluence.int.net.nokia.com/pages/viewpage.action?spaceKey=5GFTUlm&title=Sherpa+-+graphical+tool+for+Uplane+logs

## Slide 32
Sherpa – Examples
Log -> FDD_2_sherpa
2 modes:
Micro
  Scheduling per tti
  Control flows, Sizes flows
Macro
  Charts
  Stats

## Slide 33
DDR4/IQ data L1 capture – CPRI ONLY !
For L1 logs capturing -> Loner Problem Solving
For DL: Example command for one frame, execute it on loner:
asp-5c:~# snapshot --end_addr 0x412BFFFC leka_tx_0
Example command for maximum capture size (this big file can cause reset, check file system space with command: df .):
asp-5c:~# snapshot --end_addr 0x57FFFFFC leka_tx_0
For UL: Example command for two frames:
asp-5c:~# snapshot --end_addr 0x412BFFFC leka_rx_0
Example command for maximum capture size (this big file may cause reset, check file system space with command: df):
asp-5c:~# snapshot --end_addr 0x57FFFFFC leka_rx_0

## Slide 34
Triggered I/Q Capture on Loner (only 5G19A and later) – CPRI ONLY !
Example for PRACH MSG 1 Capture
Disable capture on event in webEM or webUI L1-IQ capture configuration.
Untick the box named "Enable capture on event". Select Operation option Configure.
Locate 2 files in loner
/etc/5g-layer-1/test_modes.conf
/etc/5g-layer-1/rd_parameters.conf
4. Edit test_modes.conf
prach_snapshot_test_mode = 1
5. Edit rd_parameters.conf
prach_peak_metric = x.y
You can find suitable values on BIP capture with filter:
UlData_PrachReceiveInd.detectedPrachPreambles_item_63.peakMetric > x.y
This is threshold value. The trigger will occur on any peak metric value that is bigger than x.y.

## Slide 35
Triggered I/Q Capture on Loner (only 5G19A and later) – CPRI ONLY !
Select subcell in webEM or webUI antenna snapshot configuration.
Enable capture on event in webEM or webUI L1-IQ capture configuration. Select Operation Configure and tick box "Enable capture on event". Press "Apply configuration" button.
Start the test.
Wait for the trigger to occur. Log into Loner and wait until this command shows something:
journalctl -f | grep "UTU BCN"
Wait 2 minutes so that the IQ capture files are fetched automatically from Loner.
Take a snapshot after the fault occurred.
The IQ captures will be in the snapshot in file named *_IqSamples.tgz.
Moore examples : https://confluence.int.net.nokia.com/pages/viewpage.action?pageId=851069961

## Slide 36
DDR4/IQ data – decoding TigerSailor
Tbd ->tiger sailor (license problem)
Confluance: https://confluence.int.net.nokia.com/display/5GSH/Trace+Analysis+004%3A+TigerSailor+for+analyze+antenna+IQ+signals

## Slide 37
DDR4/IQ data – decoding Dragon Decoder
Download:
Confluance: https://confluence.int.net.nokia.com/display/5GSH/Trace+Analysis001%3A+Dragon+Decoder+for+DDR4+IQ+data+decode
Examples: https://confluence.int.net.nokia.com/display/5GSH/Trace+Analysis+01%3A+Dragon+Decoder+for+DDR4+IQ+data+decode

## Slide 38
MUE TDD examples
TDD_MUE_log1 (log)
  [1]5GC000523_D_CSI_RS_CSI_reports_check_MultiUE_4UE_UE_ULDL_goodRF_aBF
2. TDD_MUE_13UE (log)
  [1]5GC000523_E_Configurable_CSI_Periodicity_80sl_13UEs_aBF
3. TDD_MUE_proact (log)
  [1]5GC000523_AB_Multi_UE_ULDL_Proactive_Scheduling_mmWaves
4. TDD_MUE_mRACH (log)
  [1]5GC000523_E_RACH_Priority_Handling_2UEs_aBF

## Slide 39
MUE FDD examples
1. FDD_1_4UE (log)
  [1]5GC001178_BE_5_SR_handling_1UE_UL_20MHz_bandwidth
2. FDD_1_4UE (log)
  [1]5GC001178_BE_1_2UE_Attach_20MHz_bandwidth
3. FDD_4_MCS_PRB (log)
  [1]5GC001178_BE_8_MCS&PRB_Reduction_4UEs_UL_varRC_20MHz_bandwidth
4. FDD_3_Proact (log)
  [1]5GC001178_BE_13_Proactive_scheduling_4UEs_20MHz_bandwidth

## Slide 40
LA FDD examples
1. FDD_5_DL_LA (log)
  [1]5GC001796_EB_TC18_DL_LA_64QAM-table_MIMO_4x4_PTRS-ON_from_Near_to_Edge_Cell_radio_condition_BW-15MHz_SA
2. FDD_4_MCS_PRB_DL_LA (log)
  [1]5GC001796_EB_TC30_UL_LA_64QAM-table_PTRS-ON_from_Edge_to_Near_Cell_radio_condition_BW-15MHz_SA

## Slide 41
Q&A

## Slide 42
Useful links
https://www.google.com/
https://confluence.int.net.nokia.com/ -> Search
ShareTechNote
http://www.sharetechnote.com/html/5G/Handbook_5G_Index.html
gNB internal communication
5G19B_e2e_internal_communication
NR Throughput Tool
http://5gtables.eecloud.dynamic.nsn-net.net/nrTput.php?code=EUQBAEAAAAAEAwAAAAAAAAAA
NR frequency band
http://niviuk.free.fr/nr_band.php
5G Uplane Sw Arch doc
https://5gwebserver.eecloud.dynamic.nsn-net.net/CinqG/uplaneSwDoc/docGen/doc/All_UplaneSwArchiDoc.html#_debugging_guide